## Slide 1: GUVM test bench Architecture

## Slide 2
GUVM_driver
Top
Test
Env.
Agent
GUVM_scoreboard
GUVM_Interface
GUVM_sequence
GUVM_seq_item
Sequencer
Target_seq_item
leon_seq_item
amber_seq_item
riscy_seq_item
GUVM_monitor
Leon_interface
Amber_interface
Riscy_interface
DUT
Leon_DUT
Amber_DUT
Riscy_DUT
GUVM_result_transaction
GUVM_seq_item
write_to_monitor
GUVM_seq_item
GUVM_seq_item
Generic UVM for Soft Processors

## Slide 3: GUVM Test bench Packages
The full Packages file consists of the three DUT processor packages, such that each package includes all the processor instructions and its format mapping. Then each package is included in the target package to grantee the test bench reusability .

## Slide 4: Packages
Target_pkg
Leon_pkg
Amber_pkg
Riscy_pkg
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
`include GUVM.sv
`include GUVM.sv
`include GUVM.sv

## Slide 5: GUVM components

## Slide 6: GUVM Test
The GUVM Test is the top-level UVM Component in the UVM Test bench.
The GUVM Test Instantiates the top-level environment, configures the environment (via factory overrides or the configuration database), and applies stimulus by invoking GUVM Sequences through the environment to the DUT processor.

## Slide 7: GUVM Environment
The UVM Environment is the higher-level verification and hierarchical component that groups together other verification components that are interrelated. It consists of GUVM Agent, GUVM Scoreboard and GUVM Monitor.
The top-level UVM Environment encapsulates all the verification components targeting the DUT processor. The configuration of the environment enables customization of its topology and behavior.
The GUVM environment is the generation of the constrained random traffic to stimulate the DUT processor, monitoring of the DUT processor response and checking of the ongoing traffic.

## Slide 8: GUVM Agent
The GUVM agent is the hierarchical component that contains other verification components that are dealing with the DUT interface.
UVM Agent includes the GUVM Sequencer and GUVM Driver.
The GUVM agent is an active agent, such that it stimulates the DUT processor by driving transactions according to the specified test scenario.

## Slide 9: GUVM Sequencer
The GUVM sequencer controls the flow of UVM Sequence Items transactions generated by the GUVM Sequences.

## Slide 10: GUVM Sequence And GUVM Transaction
GUVM Sequence is the base transaction object being sent around from the Sequencer to the Driver, from the Driver to the Scoreboard --This object holds all the instruction and the generated data.
GUVM Transaction is being sent around and from from the Sequencer to the Monitor to the Scoreboard. It holds all the output related data.

## Slide 11: GUVM Driver
The GUVM Driver receives the sequence Item transactions from the GUVM Sequencer and applies it on the DUT processor Interface.
GUVM Driver first resets the DUT processor then sends the data and the instruction to the DUT processor, as it converts the transaction-level stimulus into pin-level stimulus. It also has a TLM port to receive transactions from the Sequencer and send them to the DUT processor.

## Slide 12: GUVM Monitor
The GUVM Monitor samples the DUT interface and captures the information there in transactions that are sent out to the rest of the UVM test bench for analysis. It also extends abstraction levels by converting pin-level activity to transactions. In order to achieve that, the UVM Monitor access the DUT processor interface and also has a TLM analysis port to broadcast the created transactions through. The UVM Monitor delegate the transactions produced to the scoreboard connected to the monitor's analysis port.

## Slide 13: GUVM Scoreboard
The GUVM Scoreboard checks the behavior of the DUT processor. It receives the transactions that carries inputs and outputs of the DUT processor through GUVM Driver and GUVM Monitor analysis ports, such that it checks the signals and reports the verification.
GUVM Scoreboard gets only from the driver the data about what instruction was sent to the DUT and the generated data from the sequencer, and from monitor it gets the output signals from the DUT processor as well.
The input instruction is decoded and processed in the DUT processor and then the output signals from the monitor are compared to the expected output signals.

## Slide 14
This project milestone covers basic testing and understanding of the design.
It provides a roadmap to be followed for the future work.
At this stage, The ADD instruction is tested for the three processors.
The process of verification has been divided into: testing of individual DUT processor, detailed testing of the instruction for the three DUT processors.
Constrained random verification is used for instruction testing and data generation. Also specifically timing for the pipeline stages was considered.
Then the verification results have been displayed by the scoreboard.