## Slide 1
Project title:
Generic UVM for Soft Processors
Follow-up Thread

## Slide 2: Agenda
Introduction & History
Problem Definition
Objective
Related Work
Contribution
Proposed Solution
Results
Comparison with related work
Demo
Conclusion & Future work

## Slide 3
Introduction And History
During the past decade, the time spent by the verification engineers to verily the functionality of the designs rose to more than 60% of the total project time. Even developers of smaller chips and FPGAs are having problems with the past verification approaches. It has become more difficult to get our goal of verification using conventional verification techniques.
In addition to that, processor verification is considered to be one of the most challenging problems facing verification engineers. The processor verification process begins with creating a verification plan. As, it is the process of defining functional coverage models and functional specifications of the verification.
Furthermore, the testing strategy is one of the major decisions taken in the verification planning phase. Directed testing is well suited for testing single functionalities, but it is hard to hit more complex scenarios using only directed testing.
On the other hand, constrained-random verification (CRV) can be very effective in tackling processor verification challenges, such as: complex instruction sets, multiple pipeline-stages, in-order or out-of-order execution strategies and multi-precision operations.
The most important module of a CRV environment is the test-case generator, a test-case generator generates a large set of valid test cases in a pseudo-random way controlled and guided by constrained randomness. The development of such test generators has started to catch attention of functional verification engineers, and researchers since the early 2000s.

## Slide 4
Due to the poor features of Hardware Description Languages (HDLs) available back then, Verilog and VHDL, in terms of verification and software, the development of these generators have been categorized as a software problem.
However, recent efforts have been exerted towards the utilization of System Verilog features as a Hardware Verification Language (HVL) to improve stimulus generation quality.
The Universal Verification Methodology (UVM) gradually dominates the verification world, as it covers these needs.
UVM is a powerful verification methodology that was designed to be able to verify a wide range of design sizes and design types.
UVM is derived mainly from the OVM (Open Verification Methodology) and the (VMM) Verification Methodology Manual. It is an open source SystemVerilog library allowing creation of flexible, reusable verification components and assembling powerful test environments utilizing constrained random stimulus generation and functional coverage methodologies.
Introduction And History

## Slide 5
Problem Definition
Due to the long time spent by the verification engineers to verify the functionality of any design using ordinary verification plans consumes, and due to the huge functional space and the design complexity of a processor. Even after using OVM and UVM with the verification process nowadays, we still need something as generic and reusable as possible; so that we can reach the golden dream: only one reusable verification methodology; to save effort, time and cost.

## Slide 6
Objective
The objective of our project is: only one generic UVM used to verify the functionality of any open-source cores (soft processors), based on different ISAs and having different number of pipeline stages.

## Slide 7
Related Work
A lot of efforts have been exerted over the years to face the processor verification challenge. therefore UVM is a reusable environment such that any component can be built by extending the parent class from UVM package. Most of all the available related work implements UVM environment just for specific IP or even a microprocessor, but in our project we have made a proof for new concept which is implementing a generic UVM environment for three different microprocessors based on different ISA, pipeline stages, types of buses between processor and memory.
The main references that guided us during our milestone were:
UVM primer tutorial for a complete reusable tiny ALU by Ray Salemi.
UVM enviroment for MIPS microprocessor.

## Slide 8
The team members: Kholoud Mahmoud, Randa Ahmed, Karim Ayman, Mostafa Ayman, Waleed Samy and Yasser Ibrahim.
The contributions (till this point of the time plan):
Contribution
Task | Description | Contributors
Task #1 | Survey | All the team members
Task #2 | Ri5cy core verification plan | All the team members
Task #3 | Leon 2.4 core verification plan | Randa, Karim and Mostafa
 | Amber a23/a25 core verification plan | Kholoud, Waleed and Yasser
 | The general verification plan | All the team members
Task #4 (1st milestone in the implementation) | Implementing the Sequencer | Karim and Mostafa
 | Implementing the Driver and the Interface | Waleed and Yasser
 | Implementing the Monitor | Kholoud
 | Implementing the Scoreboard | Randa
 | Editing, connecting the components of the test bench together, debugging and testing | All the team members

## Slide 9
Proposed Solution
The user can use our generic UVM with any core (soft processor) of our three cores (or any available core with the same specifications) after attaching only 2 things to the test bench:
The core package: includes all the core instructions and its format mapping.
The core interface:
(1) includes the ports of the top-level module (core interface)
(2) each interface has functions that the driver use to drive instructions or data to the DUT
(3) deals with clk and timing to deal with each processor regarding the timing constraints.
The generic UVM Test Bench
X Package
X Interface

## Slide 10
Results
The desired output of the project is: only one generic UVM used to verify the functionality of three different open-source cores (soft processors), based on three different ISAs and having different number of pipeline stages (Ri5cy, Leon 2.4 and Amber a23/a25).
Until now, we’ve successfully reached our first milestone of the implementation of our generic UVM: a fully functional generic UVM to test the functionality of one instruction with our three different DUTs, the rest of the instructions will need just some changes in the timing inside the interface functions (to reach the critical path).
The architecture of our generic UVM test bench is represented in the next slide.

## Slide 11
GUVM_driver
top
GUVM_test
GUVM_env
GUVM_agent
GUVM_scoreboard
GUVM_interface
GUVM_sequence
GUVM_sequence_item
Sequencer
target_seq_item
leon_seq_item
amber_seq_item
riscy_seq_item
GUVM_monitor
leon_interface
amber_interface
riscy_interface
DUT
Leon DUT
Amber DUT
Riscy DUT
GUVM_result_transaction
target_seq_item
write_to_monitor
target_seq_item
target_seq_item
Generic UVM for Soft Processors Test Bench Architecture
`
include GUVM.sv
Instruction_enums
Get_format function
Specified data or instruction
of each processor
include GUVM.sv
Instruction_enums
Get_format function
Specified data or instruction
of each processor
include GUVM.sv
Instruction_enums
Get_format function
Specified data or instruction
of each processor
target_pkg
leon_pkg
amber_pkg
riscy_pkg

## Slide 12
Comparison with the Related Work
In our project, we put our scenario of verification in order to be suitable with the nature of the three different DUTs and their ISA. Definitely this done by the help of the researches and papers done discussing UVM but implementing generic environment is totally done by our team.

## Slide 13
Demo
//

## Slide 14
Conclusion & Future work
Now , we can conclude that implementing a complete generic UVM environment that is reusable for any soft processor core using its own package and interface isn’t an impossible thing , such that our project has already proved this concept. The next step is to:
complete verifying all the remained instructions in the three cores based on our generic verification plan that includes all the common and uncommon instructions.
Make sure that our environment responds to all positive & negative tests.
Future work:
Making complete coverage for the three DUTs.
Applying the concept of generic environment in a complete SoC.