## Slide 1: GUVM test bench architecture

## Slide 2
GUVM_Driver
Top
Test
Env.
Agent
GUVM_Scoreboard
GUVM_Interface
GUVM_Sequence
GUVM_seq_item
Sequencer
Target_seq_item
Leon_seq_item
Amber_seq_item
Riscy_seq_item
GUVM_Monitor
Leon_Interface
Amber_Interface
Riscy_Interface
Dut
Leon_Dut
Amber_Dut
Riscy_Dut
Transaction
Sequence_item

## Slide 3: Packages
Target_pkg
Leon_pkg
Amber_pkg
Riscy_pkg
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
Instruction_enums
Get_format_function
Specified data or instruction
of each processor
`include GUVM.sv
`include GUVM.sv
`include GUVM.sv

## Slide 4: GUVM components

## Slide 5: GUVM Test
The GUVM Test is the top-level GUVM Component in the UVM Test bench.
The UVM Test Instantiates the top-level environment, configures the environment (via factory overrides or the configuration database), and applies stimulus by invoking GUVM Sequences through the environment to the DUT processor.

## Slide 6: GUVM Environment:
The UVM Environment is the higher-level verification and hierarchical component that groups together other verification components that are interrelated. It consists of GUVM Agent and GUVM Scoreboard.
The top-level UVM Environment encapsulates all the verification components targeting the DUT processor. The configuration of the environment enables customization of its topology and behavior.
The GUVM environment is the generation of the constrained random traffic to stimulate the DUT processor, monitoring of the DUT processor response, check of ongoing traffic.

## Slide 7: GUVM Agent
The GUVM agent is the hierarchical component that contains other verification components that are dealing with the DUT interface.
UVM Agent includes the GUVM Sequencer,UVM Driver. However, the verification components may contain a few agents.
The GUVM agent is an active agent, such that it stimulates the DUT processor by driving transactions according to the spicfied test scenario.

## Slide 8: GUVM Sequencer
The GUVM sequencer controls the flow of UVM Sequence Items transactions generated by the GUVM Sequences.

## Slide 9: GUVM Sequence

## Slide 10: UVM Driver
The GUVM Driver receives the sequence Item transactions from the GUVM Sequencer and applies it on the DUT processor Interface.
GUVM Driver resets first the DUT processor then sends the data and the instruction to the DUT processor, as it converts the transaction-level stimulus into pin-level stimulus. It also has a TLM port to receive transactions from the Sequencer and send to the DUT processor.

## Slide 11: UVM Monitor

## Slide 12: UVM Scoreboard
The GUVM Scoreboard checks the behavior of the DUT processor. It receives the transactions that carries inputs and outputs of the DUT processor through GUVM Driver and GUVM Monitor analysis ports, such that it checks the signals and reports the verification.
GUVM Scoreboard gets only from the driver the data about what instruction was sent to the DUT and the generated data from the sequencer, and from monitor it gets the output signals from the DUT processor as well.
The input instruction is decoded and processed in the DUT processor and then the output signals from the monitor are compared to the expected output signals.